## Slide 1
Tracker Powering Points
Satish Dhawan, Yale University
Richard Sumner , CMCAMAC LLC
ATLAS ITK week September 14-18, 2015 @ CERN, Geneva, Switzerland.

## Slide 2
System Testing
DcDc Converter @ Yale . Tracker work stopped in 2009
Thickness of Converters – Shield thickness!
Tests @ Yale with FEAST 2 Chip mini-Module
ATLYS readout
Reduce mass/noise by using Fiber Carbon composite
(it works at higher frequencies but may be marginally useful at 2 MHz)
Prospects for Future
Lower Mass @ 5 MHZ
Topology Change Charge pump, Buck or something else?
GaN

## Slide 3
Old Cards
Liverpool Test
Paris Tweep 2009 –
US Atlas Decided in favor of Serial Power. Funding > zero
CERN Developed Toroid Inductors & FEAST Chip
UK Groups (Liverpool & RAL).
Requested a design with the YALE Planar Inductor.
Compare using the same commercial Chip as Toroid Design

## Slide 4
Vin_C
Vin_B
GND
GND
Vout_C
Vout_A
GND
Vin_A
GND
GND
GND
Vout_B
GND
GND
Vin_D
Vout_D
Ver. 1
Spirals with LTC Chip
Same Circuit as for Toroid
but different PCB Layout

## Slide 5: Planar Coil – “Up Close and Personal”
Double Trigger Noise (DTN)
Reference measurement (CERN STV10 converter) @ 0.5fC
Approx <3mm from wire bonds with improved reference @ 0.5fC
CERN converter registers zero occupancy until 0.5fC,
then registers 528/244 hits
For conducted noise configuration, Planar
coil registers zero occupancy(even at 0.5fC)
Only when close to asics are hits registered,
3/2 counts at 0.5fC, see above
With Toroid Converter
With Planar Converter
Noise in Electrons Measured @ Liverpool
cern stv10 noise 589, 604 average = 601
yale planar noise 587, 589 average = 588
noise with dc supplies (no dcdc) = 580
assuming the noise adds in quadrature, extract noise due to dcdc converter:
cern stv10 Additional noise = 157
yale planar Additional noise = 96
Planar Converter uses the same components except Inductor coil
Comments inserted by Yale University
Thickness of stv = 8 mm vs 3mm for Planar
Shield to Silicon strips are Electrostatics & Eddy current
Bottom side shield 2 mm from Planar coil traces
Can be mounted on the sensor with 50 µm Kapton
Cooling via sensor
Above picture is Double trigger noise
i.e. after a hit ; spurious counts are registered
CERN stv
Yale Planar
Ashley Greenall , UK Group
US ATLAS Moved towards Dc-Dc.
ATLAS Phase II Strip Tracker Meeting (3-7 February 2014, IFIC-Valencia, Spain)
Notes: 5

## Slide 6
Noise Couplings
Electrostatic &
H field
Coupling/Shields

## Slide 7
P #
Yale E-2158
D
Vin_B
GND
B
GND
Vin_D
Vout_D
GND
Vout_B
GND
Vout_C
C
A
GND
Vout_A
GND
GND
DC-DC Converter Model E-2158
Yale University
October 19, 2014
Vin_C
Vin_A
GND
GND
Each Converter PCB 10 mm x 63 mm. Different Coil Configuration
Channel D: Embedded Coil with 2 via: 687 nH, 83 mΩ
Channel C: Embedded Coil with 1 via: 703 nH, 83 mΩ
Channel B: External Coil: Wurth 540 nH* with short Leads
Channel A: External Coil: Wurth 540 nH* with short Leads
* With BK Precision LCR Meter
Ver. 2 OVAL / Spirals with LTC Chip

## Slide 8
Embedded Spirals
Disabled for the hand wound coil
Height = 2 mm plus shield
Toroid Inductor with Shield on toroid
height = 8 mm
Toroid vs Planar Coil
Lower Mutual Coupling if turns are further apart but adds to DC Resistance
Wurth Coil 5 mm x 8 mm
9 turns (3 layers with 3 turs)
750 nH
July 2015
Toroid Inductors Designs- Round & Elliptical
Wurth Coil 5 mm x 8 mm
Circa 2008
Coils squeezed in one direction for Mechanical
Ver 1
Spirals

## Slide 9
 | toroid radius | coil radius |  |  | wire length | R | wire dia | volume | mass
toroid coil | mm | mm | turns | L | mm | mOhms | mm | cubic mm | grams
 | 4.5 | 1.7 | 32 | 413 | 342 | 32.5 | 0.48 | 129 | 1.1
planar coil | coil length |  |  |  |  |  |  |  | 
same L, same Ohms | 1.0 | 5.4 | 6 | 415 | 203 | 34.4 | 0.36 | 58 | 0.5
Same L, same mass of Copper | 1.0 | 5.4 | 6 | 415 | 203 | 8.5 | 0.72 | 115 | 1.0
same mass, same Ohms | 1.0 | 5.5 | 9 | 967 | 311 | 33.0 | 0.46 | 111 | 1.0
Comparison of toroidal inductor and planar inductor

## Slide 10
Yale RLS 1
Using Bigger components for hand soldering
ABC130 Pwr Bd Plus MUX Liverpool
Using smallest components
Wurth Elektronik
Custom Wound
3 turns x 3 layers = 9 turns
Produced > 100 pieces
Inductor / coil
740 nH / 38.5 mΩ
Ver 3 Squeezed Oval shape for 130 nm Stave design

## Slide 11
Field Leakage ???
Close to the Cu Surface
Eddy Current Shield
From WWW
Shield Thiness ≈ Conductivity of Shield
Power Loss ≈ Resistivity of Shield Material
Notes: H: probe mapping close to the shield inhomogeneity

## Slide 12
Far side Shield H3H: Half Oz/ 3 mil thick/ Half Oz
4 Types of Near Side Shield
Half Oz/ 3 mil thick/ Half Oz
One Oz/ 3 mil thick/ One Oz
One Oz/ 5 mil Thick/ Zero Oz
One Oz/ 10μm/ One Oz
Translation Stage
Shaft
Coil under Test
Center of Coil
Probe2 100A Beehive 0.40 inch loop
1.27mm
Support
Far Side Shield
1 mm
Near Side Shield
Side View
Eddy Current Shield Measurements
Idc Change ≈ Eddy Losses
Twisted Pair
Top view
Driver Panel (encased in an Aluminum box)
A
Near Side Shield
Coil under Test
Far Side Shield
10V Power Supply
Fluke Digital Multimeter
Translation Stage
The Shields

## Slide 13
PGS (Pyrolytic Highly Oriented Graphite Sheet) is made of graphite with a structure that is close to a single crystal, which is achieved by the heat decomposition of polymeric film.
PGS is a competitive conductive sheet with high thermal conductivity.
Intrigued by this Chart
Attenuates High Frequencies

## Slide 14
Air
9 µm cu
LBL Carbon
Oxford Carbon
P4 Fermilab
P7 PGS
H Field Attenuation with Gap Material
Sample Material/ Attenuator
RLS1 converter
Wurth Coil
Beehive H Field Probe 100A 0.4 inch Dia.
To TDS 3014B Scope
1 cm
August 22, 2015
Vertical scale is different

## Slide 15
Chart: Resistance vs Frequency HP 4191A Impedance Analyzer 1- 1000 MHz
| 1.0 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
Air Ohms | 0.29 | 0.618 | 0.768 | 0.891 | 1.014 | 1.1024 | 1.28 | 1.47 | 1.67 | 1.8
Carbon strip Ohms | 0.325 | 0.53 | 0.703 | 0.802 | 0.894 | 0.986 | 0.98 | 1.324 | 1.61 | 1.85 | 2.08 | 2.29 | 2.49 | 2.69 | 2.89
P4 | 0.4 | 0.95 | 1.24 | 1.44 | 1.61 | 1.76 | 1.9 | 2.03 | 2.16 | 2.3
P7 | 0.4 | 0.89 | 1.21 | 1.47 | 1.68 | 1.88 | 2.06 | 2.24 | 2.41 | 2.6
P14 | 0.28 | 0.675 | 0.785 | 0.853 | 0.918 | 0.994 | 1.08 | 1.18 | 1.3 | 1.42
H/3/H | 0.274 | 0.283 | 0.323 | 0.404 | 0.444 | 0.479 | 0.59
Coil Under Test
With SMA connector

## Slide 16
Chart: Real part of Z @ 1 MHz
| 4.0 | 36.0 | 98.0
Air | 280.2 | 230.2 | 269.7
P14: 9 µm Cu | 516 | 404.2 | 293.5
Carbon strip | 537 | 408 | 369.9
P4: Fermilab | 536.1 | 428.8 | 377.6
P7: Pyrolytic | 531.3 | 412.8 | 337.6
Chart: Inductance @ 1 MHz
| 4.0 | 36.0 | 98.0
Air | 666 | 666.4 | 667
P14: 9 µm Cu | 511.2 | 557.9 | 636.7
Carbon strip | 643.7 | 655.3 | 657.5
P4: Fermilab | 642.5 | 650.1 | 657.4
P7: Pyrolytic | 646.9 | 655.4 | 662.3
QuadTech LCR 1 MHz
?

## Slide 17
Chart: Inductance vs Frequency
| 10.0 | 100.0 | 600.0 | 800.0 | 1000.0
Air | 770.1 | 767.9 | 682.7 | 673.9 | 666
P14: 9 µm Cu | 764.6 | 729.1 | 506.7 | 511.5 | 511.2
Carbon strip | 754.7 | 761.6 | 672.3 | 658.3 | 643.7
P4: Fermilab | 756.3 | 756.7 | 671.3 | 654.3 | 642.5
P7: Pyrolytic | 756.5 | 757.2 | 674.6 | 657 | 646.9
Yale Hand Held BK Precision LCR Meter Shows no effect
Maximum Frequency 100 KHz
Chart: Real part of Z vs frequency
| 10.0 | 100.0 | 600.0 | 800.0 | 1000.0
Air | 42 | 55.3 | 211.53 | 246.6 | 280.2
P14: 9 µm Cu | 43.1 | 86.3 | 503.3 | 493 | 516
Carbon strip | 42.6 | 58.2 | 327.4 | 413.7 | 537
P4: Fermilab | 42.5 | 58.9 | 326.6 | 424.6 | 536.1
P7: Pyrolytic | 42.6 | 59.4 | 328.1 | 429.1 | 531.3
QuadTech LCR 1 MHz

## Slide 18
Wurth Coil | Curremt | Spacers |  |  |  |  |  |  | 
Shield | mA | Black Mylar = 6 mils each > total = ~30 mils |  |  |  |  |  | FR4 Spacers | 
 |  | 1 | 2 | 3 | 4 | 5 | 32 mils | 62 mils | 2 x 62 mils
Air | 30.650 |  |  |  |  |  |  |  | 
Carbon strip | 37.010 | 35.72 | 34.75 | 34.12 | 33.49 | 32.96 | 33.53 | 32.29 | 31.04
P4: Fermilab | 37.160 | 36.08 | 35.11 | 34.16 | 33.55 | 32.51 | 33.74 | 32.32 | 31.26
P7: Pyrolytic | 37.810 | 36.25 | 34.46 | 33.7 | 33.58 | 32.93 | 33.37 | 31.7 | 31.02
P14: 9 µm Cu | 37.860 | 34.12 | 33 | 32.41 | 32 | 31.72 | 31.93 | 31.04 | 30.78
H/5/H | 33.440 | 32.62 | 32.26 | 31.78 | 31.58 | 31.32 | 31.54 | 30.9 | 30.72
Converter RLS1 With Feast2 Chip
Wurth Coil
Insulator 6 mils
Measure DC Current drawn by Feast2 chip vs
Shield material and distance/gap from top of coil
Shield Samples
Chart: DC-DC input current (no load)
| 0.0 | 6.0 | 12.0 | 18.0 | 24.0 | 30.0 | 62.0 | 128.0
Air | 0.65 | 0.65 | 0.65 | 0.65 | 0.65 | 0.65 | 0.65 | 0.65
Carbon strip | 7.01 | 5.72 | 4.75 | 4.12 | 3.49 | 2.96 | 2.29 | 1.04
P4: Fermilab | 7.16 | 6.08 | 5.11 | 4.16 | 3.55 | 2.51 | 2.32 | 1.26
P7: Pyrolytic | 7.81 | 6.25 | 4.46 | 3.7 | 3.58 | 2.93 | 1.7 | 1.02
P14: 9 µm Cu | 7.86 | 4.12 | 3 | 2.41 | 2 | 1.72 | 1.04 | 0.78
H/5/H | 3.44 | 2.62 | 2.26 | 1.78 | 1.58 | 1.32 | 0.9 | 0.72

## Slide 19
Coil on Top may induce noise into FEAST Chip via the wire bonds & PCB Traces
130nm Mini Module
x-ray of Feast2 Chip
Liverpool Power Board with Shield down
Atlys Board + Interface
Yale RLS1 Power Bd. with Shield down
Wire bonds: secondary of transformer for H field

## Slide 20
Yale Run 62 Test Results – August 07, 2015
RLS1 with P4(grounded) with 9 µm Cu Foil added & grounded
Yale Run 61 Test Results – August 07, 2015
RLS1 with P4 (grounded)
Seek Ashley & Peter’s Help

## Slide 21: Further Work Investigate / Goals Shield with Carbon+Copper (Carbon closer to Inductor)
With shielding we replicate noise numbers as quoted by Ashley
Slope should be the other way around
Understand pickup sensitivity of the sensors

## Slide 22
Acknowledgements
Adrian Au
Savannah Thais
DR. Eric Paulson
Prof. Keith Baker
Prof. Steven Lamoreaux

## Slide 23
THE END
Questions Please?
Back up Slides

## Slide 24
Seminar 9: Wireless charging of EV
Chris Mi . U of Michigan
Al Plate 600 mm x 800mm 1 mm thick for mechanical strength
Coil - Bottom
Coil - Top
Car Metal
Frequency = 85 KHz
Power transmitted = 10KW
Inefficiency without Al shield = 20 %
Inefficiency with Al shield = 1 %
Power loss in Car metal without Al shield = 2 KW > 15C rise in temperature
Power loss in Al shield = 0.1 KW
Yale University
March 21, 2014
http://www-personal.engin.umd.umich.edu/~chrismi/